## Slide 1: Capability-Based Memory Protection for Scalable Vector Processing
or “the quest for secure vectorized memcpy”
Presentation for RISE Student Competition 2022
Samuel Stark - sws35@cam.ac.uk
M.Phil project @ University of Cambridge, 2021-2022
Notes: Hi! I’m Samuel, today I’m going to talk about my Masters project on “Capability-Based Memory Protection for Scalable Vector Processing”, which in practice ended up as “the quest for secure vectorized memcpy”.
First, what is capability-based memory protection?

## Slide 2: Applying CHERI to Vector Processors
or “the quest for secure vectorized memcpy”
Presentation for RISE Student Competition 2022
Samuel Stark - sws35@cam.ac.uk
M.Phil project @ University of Cambridge
Notes: Hi! I’m Samuel, today I’m going to talk about my Masters project from last year on “Capability-Based Memory Protection for Scalable Vector Processing”, which in practice ended up as “the quest for secure vectorized memcpy”.
First, just for the purposes of time, I’m going to simplify the title – this is really about applying CHERI (a project that I will explain in a moment) to the general concept of vector processors.

## Slide 3: Capability-Based Memory Protection = CHERI
Most architectures are integer-addressed
  Inherently insecure – integers are forgeable
  Code can dereference any address at any time
CHERI is a project that addresses this
  Capability Hardware Enhanced RISC Instructions
CHERI architectures use unforgeable tokens/capabilities instead
Notes: Well, it’s a practice that addresses an inherent security flaw of integer-addressed memory.
In most architectures, every piece of data in memory has a numerical address associated with it
and any piece of code in your program can just make up that number and access that data, even if it wasn’t supposed to.
Essentially, integer addresses are forgeable.
CHERI is a project from the University of Cambridge that fixes this - CHERI-based architectures use unforgeable tokens i.e. capabilities as addresses instead.
What that means in practice, is that every piece of data, be it (click) a register or main memory, is associated with a (click) tag bit that determines if it (click) is an integer or a capability.

## Slide 4: CHERI?
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
main memory
...
Notes: Well, it’s a practice that addresses an inherent security flaw of integer-addressed memory.
In most architectures, every piece of data in memory has a numerical address associated with it
and any piece of code in your program can just make up that number and access that data, even if it wasn’t supposed to.
Essentially, integer addresses are forgeable.
CHERI is a project from the University of Cambridge that fixes this - CHERI-based architectures use unforgeable tokens i.e. capabilities as addresses instead.
What that means in practice, is that every piece of data, be it (click) a register or main memory, is associated with a (click) tag bit that determines if it (click) is an integer or a capability.

## Slide 5: CHERI?
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
main memory
...
Notes: Well, it’s a practice that addresses an inherent security flaw of integer-addressed memory.
In most architectures, every piece of data in memory has a numerical address associated with it
and any piece of code in your program can just make up that number and access that data, even if it wasn’t supposed to.
Essentially, integer addresses are forgeable.
CHERI is a project from the University of Cambridge that fixes this - CHERI-based architectures use unforgeable tokens i.e. capabilities as addresses instead.
What that means in practice, is that every piece of data, be it (click) a register or main memory, is associated with a (click) tag bit that determines if it (click) is an integer or a capability.

## Slide 6: CHERI?
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
I
I
C
I
I
I
I
I
main memory
...
I
C
I
C
I
I
C
I
I
C
C
I
I
Notes: The hardware only allows memory access through capabilities, and each capability grants access to some finite range of memory (click).
The hardware also ensures that new capabilities cannot be pulled out of thin air or increased in scope, just that you can derive a new capability from an old one.
In this example, we have access to 5 words of memory, and we create a new capability with access to two of those five (click) or just one of those five (click), but we can’t gain access to memory outside that range.

## Slide 7: CHERI?
I
C
I
C
I
I
C
I
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
I
I
C
I
I
I
I
I
main memory
...
I
C
C
I
I
Notes: The hardware only allows memory access through capabilities, and each capability grants access to some finite range of memory (click).
The hardware also ensures that new capabilities cannot be pulled out of thin air or increased in scope, just that you can derive a new capability from an old one.
In this example, we have access to 5 words of memory, and we create a new capability with access to two of those five (click) or just one of those five (click), but we can’t gain access to memory outside that range.

## Slide 8: CHERI?
I
C
I
C
I
I
C
I
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
I
I
C
I
I
I
C
I
main memory
...
I
C
C
I
I
Notes: The hardware only allows memory access through capabilities, and each capability grants access to some finite range of memory (click).
The hardware also ensures that new capabilities cannot be pulled out of thin air or increased in scope, just that you can derive a new capability from an old one.
In this example, we have access to 5 words of memory, and we create a new capability with access to two of those five (click) or just one of those five (click), but we can’t gain access to memory outside that range.

## Slide 9: CHERI?
I
C
I
C
I
I
C
I
CHERI architectures use unforgeable tokens/capabilities instead
  All data is tagged as an integer or a capability
  Capabilities grant access to a range of memory
  Can only derive capabilities from larger capabilities
registers
I
I
C
I
I
I
C
I
main memory
...
I
C
C
I
I
Notes: The hardware only allows memory access through capabilities, and each capability grants access to some finite range of memory (click).
The hardware also ensures that new capabilities cannot be pulled out of thin air or increased in scope, just that you can derive a new capability from an old one.
In this example, we have access to 5 words of memory, and we create a new capability with access to two of those five (click) or just one of those five (click), but we can’t gain access to memory outside that range.
The moral of the story is under CHERI, code can only access memory if it has been given access memory, and that security is extremely granular

## Slide 10: CHERI?
I
C
I
C
I
I
C
I
Under CHERI,
code can only access memory
if it has been given access to that memory
registers
I
I
C
I
I
I
C
I
main memory
...
I
C
C
I
I
Notes: The hardware only allows memory access through capabilities, and each capability grants access to some finite range of memory (click).
The hardware also ensures that new capabilities cannot be pulled out of thin air or increased in scope, just that you can derive a new capability from an old one.
In this example, we have access to 5 words of memory, and we create a new capability with access to two of those five (click) or just one of those five (click), but we can’t gain access to memory outside that range.
The moral of the story is under CHERI, code can only access memory if it has been given access to that memory, and that security is extremely granular.

## Slide 11: CHERI?
Under CHERI,
code can only access memory
if it has been given access to that memory
This is extremely useful for security
Currently testing in real-world hardware (see Arm Morello)
Hasn’t addressed vectorization... yet
  No support for Arm SVE
  Need this for wider adoption
Notes: That’s an extremely useful security property, and industry has recognized this – Arm are currently manufacturing test boards with a CHERI-based ARM architecture
But there’s a lot we haven’t fully integrated with CHERI yet, and one of those things is vectorization.
This is important for CHERI’s wider adoption, because vectorized memory accesses are used.
A great example of this is memcpy.

## Slide 12: CHERI + Vectors = ?
We want to understand how CHERI interacts with vector architectures
Particularly scalable vector architectures
  Arm SVE
  RISC-V “V” extension
  These are designed to remain relevant well into the future
What mixes CHERI memory accesses with vectors?
Notes: Unnecessary slide -

## Slide 13: Vectorized memcpy
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
A
B
C
D
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 14: CHERI + Vectorized memcpy
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
A
B
C
D
capabilities
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 15: CHERI + Vectorized memcpy
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
capabilities
I
I
I
I
I
I
I
I
I
I
C
I
I
I
I
I
A
B
C
D
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 16: CHERI + Vectorized memcpy
I
I
I
I
I
I
C
I
I
I
I
I
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
capabilities
E
F
G
H
I
I
C
I
A
B
C
D
I
I
I
I
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 17: CHERI + Vectorized memcpy
I
I
I
I
I
I
C
I
I
I
I
I
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
capabilities
E
F
G
H
I
I
C
I
A
B
C
D
I
I
I
I
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 18: CHERI + Vectorized memcpy
I
I
I
I
I
I
I
I
I
I
C
I
I
I
I
I
void* memcpy( void* dest, const void* src, size_t count );
A
B
C
D
E
F
G
H
I
J
K
L
vector
registers
capabilities
E
F
G
H
I
I
C
I
A
B
C
D
Notes: Memcpy copies data from the source to the destination
When vectorized (click), multiple words are copied at once through the vector registers (click.. wait)
There are two complications introduced by capabilities: the src and dest pointers should themselves be capabilities (click), so the vector instructions need to use capability addressing, and the data being copied may itself be a mix of integers and capabilities (click).
This means the vector registers must also have tag bits (click), so capabilities can be copied through correctly (click), without creating any opportunities to forge new capabilities.

## Slide 19: Project Goals
Combine CHERI with RISC-V “V” (RVV) scalable vector extension
  CHERI+RISC-V already exists, just add RVV
Can we adapt all RVV instructions to capability addressing?
Can we amortize the cost of bounds checks?
Can we maintain source-code compatibility with legacy programs?
Can we load/store/manipulate capabilities-in-vectors?
Notes: To experiment with these problems, we chose to combine our pre-existing CHERI-RISC-V architecture with the official RISC-V vector extension RVV.
We faced four major challenges:
- RVV memory instructions use multiple addressing modes, and we wanted to adapt all of them to capabilities. This was entirely successful.
- we checked some performance concerns: Each memory access has to be checked against the capability bounds. We found that in most cases you can combine the checks for multiple elements and amortize the cost, except under the indexed addressing mode and other edge cases.
- we looked at source-code compatibility – CHERI strives to ensure that old code can be recompiled for CHERI and just work without changes where possible, and we maintained that here in most cases except for code using inline assembly.
- finally we determined we can hold capabilities-in-vectors, implement memcpy, and even add some minimal capability manipulation inside the vector registers.

## Slide 20: Project Goals
Combine CHERI with RISC-V “V” (RVV) scalable vector extension
  CHERI+RISC-V already exists, just add RVV
Can we adapt all RVV instructions to capability addressing?
Can we amortize the cost of bounds checks?
Can we maintain source-code compatibility with legacy programs?
Can we load/store/manipulate capabilities-in-vectors?
✓
Notes: To experiment with these problems, we chose to combine our pre-existing CHERI-RISC-V architecture with the official RISC-V vector extension RVV.
We faced four major challenges:
- RVV memory instructions use multiple addressing modes, and we wanted to adapt all of them to capabilities. This was entirely successful.
- we checked some performance concerns: Each memory access has to be checked against the capability bounds. We found that in most cases you can combine the checks for multiple elements and amortize the cost, except under the indexed addressing mode and other edge cases.
- we looked at source-code compatibility – CHERI strives to ensure that old code can be recompiled for CHERI and just work without changes where possible, and we maintained that here in most cases except for code using inline assembly.
- finally we determined we can hold capabilities-in-vectors, implement memcpy, and even add some minimal capability manipulation inside the vector registers.

## Slide 21: Project Goals
Combine CHERI with RISC-V “V” (RVV) scalable vector extension
  CHERI+RISC-V already exists, just add RVV
Can we adapt all RVV instructions to capability addressing?
Can we amortize the cost of bounds checks?
Can we maintain source-code compatibility with legacy programs?
Can we load/store/manipulate capabilities-in-vectors?
✓
✓
Notes: To experiment with these problems, we chose to combine our pre-existing CHERI-RISC-V architecture with the official RISC-V vector extension RVV.
We faced four major challenges:
- RVV memory instructions use multiple addressing modes, and we wanted to adapt all of them to capabilities. This was entirely successful.
- we checked some performance concerns: Each memory access has to be checked against the capability bounds. We found that in most cases you can combine the checks for multiple elements and amortize the cost, except under the indexed addressing mode and other edge cases.
- we looked at source-code compatibility – CHERI strives to ensure that old code can be recompiled for CHERI and just work without changes where possible, and we maintained that here in most cases except for code using inline assembly.
- finally we determined we can hold capabilities-in-vectors, implement memcpy, and even add some minimal capability manipulation inside the vector registers.

## Slide 22: Project Goals
Combine CHERI with RISC-V “V” (RVV) scalable vector extension
  CHERI+RISC-V already exists, just add RVV
Can we adapt all RVV instructions to capability addressing?
Can we amortize the cost of bounds checks?
Can we maintain source-code compatibility with legacy programs?
Can we load/store/manipulate capabilities-in-vectors?
✓
✓
✓
Notes: To experiment with these problems, we chose to combine our pre-existing CHERI-RISC-V architecture with the official RISC-V vector extension RVV.
We faced four major challenges:
- RVV memory instructions use multiple addressing modes, and we wanted to adapt all of them to capabilities. This was entirely successful.
- we checked some performance concerns: Each memory access has to be checked against the capability bounds. We found that in most cases you can combine the checks for multiple elements and amortize the cost, except under the indexed addressing mode and other edge cases.
- we looked at source-code compatibility – CHERI strives to ensure that old code can be recompiled for CHERI and just work without changes where possible, and we maintained that here in most cases except for code using inline assembly.
- finally we determined we can hold capabilities-in-vectors, implement memcpy, and even add some minimal capability manipulation inside the vector registers.

## Slide 23: Project Goals
Combine CHERI with RISC-V “V” (RVV) scalable vector extension
  CHERI+RISC-V already exists, just add RVV
Can we adapt all RVV instructions to capability addressing?
Can we amortize the cost of bounds checks?
Can we maintain source-code compatibility with legacy programs?
Can we load/store/manipulate capabilities-in-vectors?
✓
✓
✓
✓
Notes: To experiment with these problems, we chose to combine our pre-existing CHERI-RISC-V architecture with the official RISC-V vector extension RVV.
We faced four major challenges:
- RVV memory instructions use multiple addressing modes, and we wanted to adapt all of them to capabilities. This was entirely successful.
- we checked some performance concerns: Each memory access has to be checked against the capability bounds. We found that in most cases you can combine the checks for multiple elements and amortize the cost, except under the indexed addressing mode and other edge cases.
- we looked at source-code compatibility – CHERI strives to ensure that old code can be recompiled for CHERI and just work without changes where possible, and we maintained that here in most cases except for code using inline assembly.
- finally we determined we can hold capabilities-in-vectors, implement memcpy, and even add some minimal capability manipulation inside the vector registers.

## Slide 24: Project Deliverables
Detailed answers to those questions
  Plus documentation on all relevant CHERI and RVV elements
Proposed CHERI + RVV combined specification
  Supports all RVV addressing modes
  Supports vectorized memcpy, capabilities-in-vectors
  Generalizable to (most of) Arm SVE
Example implementation (10,000 LoC)
  CHERI-RVV hardware emulator (Rust)
  CHERI-Clang fork with CHERI+RVV support (C++)
  High-coverage test programs (C)
Notes: In terms of the deliverables, of course the thesis has much more detailed answers to those previous questions, plus comprehensive documentation of CHERI and RVV
We proposed a CHERI+RVV combined specification, supporting all RVV instructions, capabilities-in-vectors, and thus vectorized memcpy.
We also determine that the principles we used can be generalized to Arm’s scalable vector extension, so it will be simple to adapt most of that to CHERI.
Finally, we created an example implementation of our specification, including a hardware emulator, compiler support, and self-checking test programs for RVV memory ops, totalling over 10 thousand lines of code.

## Slide 25: Conclusion
First public evaluation and implementation of CHERI + Vectors
Enables fast vector memory ops and memcpy on CHERI
Another roadblock to widespread adoption is gone!
More Information:
theturboturnip.github.io/cheri-rvv
Thanks for watching!
Notes: So in conclusion
- This is the first publicly available evaluation and implementation of a vectorized CHERI architecture
- It confirms that CHERI is compatible with these vector operations without loss of functionality, reduced security, or significant performance degradation.
- If this wasn’t the case, adopting CHERI would be a much greater ask for certain classes of processor, and now we have effectively eliminated this roadblock!
More details on the project are available on my website, and of course for the R I S E judges in the application form.
Thank you very much for watching!